## Slide 1: Microelectronics and VLSI IT705D
Module 2 – MOS Structure

## Slide 2: Module 2 – MOS Structure (Part I)
E-MOS and D-MOS
Charge Inversion in E-MOS
Threshold voltage and Flat band voltage
Potential balance and charge balance
Inversion, MOS Capacitance

## Slide 3: Transistor
A transistor is a semiconductor device used to amplify or switch electronic signals and electrical power. It is composed of semiconductor material usually with at least three terminals for connection to an external circuit.
There are two types of transistors,
  Bipolar transistor has terminals labelled base, collector, and emitter. A small current at the base terminal (that is, flowing between the base and the emitter) can control or switch a much larger current between the collector and emitter terminals.
  Field-effect transistor, the terminals are labelled gate, source, and drain, and a voltage at the gate can control a current between source and drain.

## Slide 4: Doping of Semiconductor
In semiconductor production, doping intentionally introduces impurities into an extremely pure intrinsic semiconductor for the purpose of modulating its electrical properties.
The impurities are dependent upon the type of semiconductor and the properties that it needs to have for its intended purpose.
Lightly and moderately doped semiconductors are referred to as extrinsic semiconductors.
A semiconductor doped to such high levels that it acts more like a conductor than a semiconductor is referred to as a degenerated semiconductor.

## Slide 5: Semiconductor Conductivity
In solid-state physics, the valence band and conduction band are the bands closest to the Fermi level and thus determine the electrical conductivity of the solid.
The valence band is the highest range of electron energies in which electrons are normally present at absolute zero temperature, while the conduction band is the lowest range of vacant electronic states.

## Slide 7: Semiconductor Types
There are three types of semiconductors,
  NMOS
  PMOS
  CMOS

## Slide 8: Semiconductor Logic (NMOS)
NMOS is built with n-type source and drain and a p-type substrate
In a NMOS, carriers are electrons
If a high voltage is applied to the gate, NMOS will conduct, when a low voltage is applied in the gate, NMOS will not conduct
NMOS are considered to be faster than PMOS, since the carriers in NMOS, which are electrons, travel twice as fast as valence band electrons (holes).
NMOS ICs would be smaller than PMOS ICs

## Slide 9: Semiconductor Logic (PMOS)
PMOS is built with p-type source and drain and a n-type substrate.
PMOS, carriers are Valence band electrons
PMOS transistors operate by creating an inversion layer in an n-type transistor body. This inversion layer, called the p-channel
If a high voltage is applied to the gate, PMOS will not conduct, when a low voltage is applied in the gate, PMOS will conduct
PMOS devices are more immune to noise than NMOS devices.

## Slide 10: Semiconductor Logic (CMOS)
CMOS means Complementary Metal-Oxide-Semiconductor Transistor. CMOS circuit contains both PMOS transistor and NMOS transistor.
Complementary metal–oxide–semiconductor (CMOS) is a technology for constructing integrated circuits.
CMOS technology is used in microprocessors, microcontrollers, static RAM, and other digital logic circuits.
CMOS technology is also used for several analog circuits such as image sensors (CMOS sensor), data converters etc.

## Slide 11: Types of Three Terminal Semiconductor
There are two major types of three-terminal semiconductor devices:
  Metal-oxide-semiconductor field-effect transistor (MOSFET)
  Bipolar junction transistor (BJT)

## Slide 12: Basic Details
Three-terminal semiconductor devices are far more useful than two-terminal ones because they can be used in many applications.
This ranges from signal amplification to digital logic and memory.
The basic principle involved is the use of voltage between two terminals to control the current flowing in the third terminal.
Also in the extreme, the control signal can be used to cause the current in the third terminal to change from zero to a large value, thus allowing the device to act as a switch.
This switch is the basis of the realization of the logic inverters, the basic element of digital circuits.

## Slide 13: FET Terminals
The FET's three terminals are:
  Source (S), through which the carriers enter the channel. Conventionally, current entering the channel at S is designated by IS.
  Drain (D), through which the carriers leave the channel. Conventionally, current entering the channel at D is designated by ID. Drain-to-source voltage is VDS.
  Gate (G), the terminal that modulates the channel conductivity. By applying voltage to G, one can control ID.

## Slide 14: Field Effect Transistor

## Slide 15: MOS Structure
The traditional metal–oxide–semiconductor (MOS) structure is obtained by growing a layer of silicon dioxide (SiO2) on top of a silicon substrate and depositing a layer of metal or polycrystalline silicon.
Fig.: MOS Structure on p-type silicon

## Slide 16: MOSFET
The metal–oxide–semiconductor field-effect transistor (MOSFET) is a common type of transistor
In MOSFET, charge carriers are either electrons [-ve] or valence band electron population (holes) [+ve], flowing along channels
It is a device used to amplify or switch electronic signals
MOSFET is by far the most common field-effect transistor in both digital and analog circuits

## Slide 17: Utility of MOSFET
MOSFET has become by far the most widely used electronic device, especially in the design of integrated circuits (ICs)
MOSFETs can be made quite small, and their manufacturing process is relatively simple
MOSFET operation requires little power
Circuit designers have found ingenious ways to implement digital and analog functions utilizing MOSFET
These properties have made it possible to pack large numbers of MOSFETs on a single IC chip to implement very sophisticated, very- large-scale-integrated (VLSI) circuits

## Slide 18: MOSFET Structure - 1
MOSFET is fabricated on a single-crystal silicon wafer
The substrate is of p-type for an n-channel MOSFET (NMOS) and n-type for a p-channel MOSFET (PMOS)
Two heavily doped regions (which will be of n-type for NMOS and p-type for PMOS) will be there which act as source and drain

## Slide 19: MOSFET Structure - 2
A thin layer of silicon dioxide ( SiO2) of thickness 2-50 nm, which is an excellent electrical insulator, is grown on the surface of the substrate, covering the area between the source and drain regions
Metal is deposited on top of the oxide layer to form the gate electrode of the device
Metal contacts are also made to the source region, the drain region, and the substrate, also known as the body

## Slide 20: Schematic of MOSFET

## Slide 21: Threshold Voltage (Vt)
The threshold voltage, commonly abbreviated as Vt, of a field-effect transistor (FET) is the minimum gate-to-source voltage differential that is needed to create a conducting path between the source and drain terminals.

## Slide 22: Flat band Voltage
The point at which an external applied voltage causes no internal potential difference across a metal oxide semiconductor structure
If there is no charge present in the oxide or at the oxide-semiconductor interface, the flat band voltage simply equals the difference between the gate metal work-function, FM, and the semiconductor work-function, FS.
VFB = FM - Fs

## Slide 23: Inversion
The complementary MOSFET is the p-type or p-channel MOSFET.
It contains p-type source and drain regions in an n-type substrate.
The inversion layer is formed when valence band electron population (holes) are attracted to the interface by a negative gate voltage. While the +ve charge carriers still flow from source to drain, they result in a negative drain current.

## Slide 24: MOSFET Classification

## Slide 25: EMOS
Enhancement mode MOSFETs don’t have a channel for current flow between source and drain.
When a voltage VDS is applied across source and drain, current flows only if the gate voltage (VGS) is large enough to create a conducting channel between source and drain by field effect. Otherwise the source and drain terminals are not connected.

## Slide 26: EMOS Schematic

## Slide 27: EMOS Operational Details
In an n-channel EMOS, one diode is formed by the pn junction between the n+ (heavily n-doped) drain region and the p-substrate, and the other diode is formed by the pn junction between the p-type substrate and the n+ source region.
These back-to-back diodes prevent current conduction from drain to source when a voltage VDS is applied

## Slide 28: EMOS Operation Regions
Cut-off or Sub-threshold or Weak Inversion Mode (VGS < Vt)
Triode Mode or Linear Region or Ohmic Mode (VGS > Vt) and VDS < (VGS - Vt))
Saturation Mode or Active Mode (VGS > Vt) and VDS > (VGS - Vt))

## Slide 29: Cut-off or Sub-threshold or Weak Inversion Mode
According to the basic threshold model, the transistor is turned off, and there is no conduction between drain and source.
In reality, the Boltzmann distribution of electron energies and allows some of the more energetic electrons at the source to enter the channel and flow to the drain, resulting in a sub-threshold current
This is an exponential function of gate–source voltage.

## Slide 30: Triode Mode or Linear Region or Ohmic Mode
VGS is above Vt, the positive static charges accumulating at the gate electrode gain enough strength to attract electrons from nearby heavily n-doped regions and thus a conducting n-channel is created.
Since such a channel is created out of a p-type substrate, the channel formed is termed as ‘inversion channel’ also.
A constant VGS above Vt, VDS appears as a voltage drop across the length of the channel. That is, along the channel from source to drain, the voltage increases from 0 to VDS.

## Slide 31: Saturation Mode or Active Mode
VDS is increased to the value that reduces the voltage between gate and channel at the drain end to Vt . That is, VGS -VDS = Vt, or VDS = VGS – Vt
The channel depth at the drain end decreases to almost zero, and the channel is said to be pinched off.
The MOSFET is said to have entered the saturation region of operation. The voltage VDS at which saturation occurs is denoted by VDSsat.
Obviously, for every value of VGS ≥ Vt, there is a corresponding value of VDSsat..

## Slide 32: Depletion mode MOSFET
Depletion mode MOSFETs have a built-in channel connecting the source and drain.
DMOS is a “normally on” device since there is no need to apply some threshold voltage at the gate terminal to induce a current carrying channel between source and drain.

## Slide 33: DMOS Operation
Current will flow through the channel with an applied voltage between source and drain as a semiconductor resistance.
However, when a negative voltage is applied to the gate for an n-channel DMOS, some negative static charge will accumulate on the gate. This negative voltage will repel electrons away from the gate.
But free electrons are the majority current carriers in the n-type silicon channel. By repelling them away from the gate region, the applied gate voltage creates a depletion region around the gate area, thus restricting the usable width of the channel for current flow.
The p channel DMOS transistor operation is the same as for the n channel DMOS transistor